NOTE: In 2009, the National Committee on Uniform Traffic Laws and Ordinances (NCUTLO), which developed and maintained the Uniform Vehicle Code (UVC), went into hiatus. This left a void that the NCUTCD believes must be filled in order for its goal of uniformity of traffic control devices to be achieved and to provide guidance on model laws and rules for States and local governments. The Rules of the Road Committee (RORC) is an ad hoc committee of the NCUTCD to address changes to the “Rules of the Road” of the UVC.

Final recommended UVC content, as approved at a regular meeting of the NCUTCD, will be posted on the NCUTCD web site as model law for use by States and local jurisdictions wishing to have their Rules of the Road consistent with the national standard.  The recommendations, not being a part of the Manual on Uniform Traffic Control Devices, have no status with the FHWA.

TECHNICAL COMMITTEE:	Rules of the Road Committee (RORC)

TOPIC: 	Relaxing the requirement for bicyclists to wait for a steady red signal

STATUS / DATE OF ACTION:

BTC Draft:	07/10/2012

BTC Approval:

Transmitted to Sponsors:	(withdrawn from May2013 sponsor distribution)

BTC Revision:

RORC Approval:

Council Approval:

ORIGIN OF REQUEST:	NCUTCD Bicycle Technical Committee

NCUTCD Rules of the Road Committee

AFFECTED SECTIONS OF UVC:	11-202

# SUMMARY:

# The proposed new section would relax the requirement for bicyclists to stop at a steady red signal

# DISCUSSION:

# A bicyclist may have no option but to proceed through an intersection on a red light, as many traffic signals are triggered by electronic actuators which do not respond to bicycles. A bicyclist may need to enter a wide intersection before the signal turns green in order to complete crossing before it turns red.  The proposed language is as in Idaho law, http://www.legislature.idaho.gov/idstat/Title49/T49CH7SECT49-720PrinterFriendly.htm

# RECOMMENDED CHANGES:

# Section 1-109 of the UVC is proposed to be modified as follows. Deletions from the 2000 UVC text are noted in strikethrough red, and insertions in underline blue.

§	11—202—Traffic—control signal legend

Whenever traffic is controlled by traffic—control signals exhibiting different colored lights, or colored lighted arrows, successively one at a time or in combination, only the colors Green, Red and Yellow shall be used, except for special pedestrian signals carrying a legend, and said lights shall indicate and apply to drivers of vehicles and pedestrians as follows:

(a)	Green indication

- Vehicular traffic facing a circular green signal may proceed straight through or turn right or left unless a sign at such place prohibits either such turn. But vehicular traffic, including vehicles turning right or left, shall yield the right of way to other vehicles and to pedestrians lawfully within the intersection or an adjacent crosswalk at the time such signal is exhibited.

- Vehicular traffic facing a green arrow signal, shown alone or in combination with another indication, may cautiously enter the intersection only to make the movement indicated by such arrow, or such other movement as is permitted by other indications shown at the same time. Such vehicular traffic shall yield the right of way to pedestrians lawfully within an adjacent crosswalk and to other traffic lawfully using the intersection.

- Unless otherwise directed by a pedestrian-control signal as provided in §11-203, pedestrians facing any green signal, except when the sole green signal is a turn arrow, may proceed across the roadway within any marked or unmarked crosswalk.

(b)	Steady yellow indication

- Vehicular traffic facing a steady circular yellow or yellow arrow signal is thereby warned that the related green movement is being terminated or that a red indication will be exhibited immediately thereafter.

- Pedestrians facing a steady circular yellow or yellow arrow signal, unless otherwise directed by a pedestrian—control signal as provided in §11—203, are thereby advised that there is insufficient time to cross the roadway before a red indication is shown and no pedestrian shall then start to cross the roadway.

(c)	Steady red indication

- Vehicular traffic facing a steady circular red signal alone shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then before entering the intersection, and shall remain standing until an indication to proceed is shown except as provided in subsection (c)3.

- Vehicular traffic facing a steady red arrow signal shall not enter the intersection to make the movement indicated by the arrow, and unless entering the intersection to make a movement permitted by another signal, shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then before entering the intersection and shall remain standing until an indication permitting the movement indicated by such red arrow is shown except as provided in subsection (c)3.

- Except when a sign is in place prohibiting a turn, vehicular traffic facing any steady red signal may cautiously enter the intersection to turn right, or to turn left from a one—way street into a one—way street, after stopping as required by subsection (c)1 or subsection (c)2. After stopping, the driver shall yield the right of way to any vehicle in the intersection or approaching on another roadway so closely as to constitute an immediate hazard during the time such driver is moving across or within the intersection or junction of roadways. Such driver shall yield the right of way to pedestrians within the intersection or an adjacent crosswalk.

- A person operating a bicycle or human-powered vehicle approaching a steady red traffic control light shall stop before entering the intersection and shall yield to all other traffic. Once the person has yielded, he may proceed through the steady red light with caution. Provided however, that a person after slowing to a reasonable speed and yielding the right-of-way if required, may cautiously make a right-hand turn. A left-hand turn onto a one-way highway may be made on a red light after stopping and yielding to other traffic.

5.4. Unless otherwise directed by a pedestrian—control signal as provided in §11—203, pedestrians facing a steady circular red or red arrow signal alone shall not enter the roadway.

(d)	In the event an official traffic—control signal is erected and maintained at a place other than an intersection, the provisions of this section shall be applicable except as to those provisions which by their nature can have no application.  Any stop required shall be made at a sign or marking on the pavement indicating where the stop shall be made, but in the absence of any such sign or marking the stop shall be made at the signal.