NOTE: In 2009, the National Committee on Uniform Traffic Laws and Ordinances (NCUTLO), which developed and maintained the Uniform Vehicle Code (UVC), went into hiatus. This left a void that the NCUTCD believes must be filled in order for its goal of uniformity of traffic control devices to be achieved and to provide guidance on model laws and rules for States and local governments. The Rules of the Road Committee (RORC) is an ad hoc committee of the NCUTCD to address changes to the “Rules of the Road” of the UVC.

Final recommended UVC content, as approved at a regular meeting of the NCUTCD, will be posted on the NCUTCD web site as model law for use by States and local jurisdictions wishing to have their Rules of the Road consistent with the national standard.  The recommendations, not being a part of the Manual on Uniform Traffic Control Devices, have no status with the FHWA.

TECHNICAL COMMITTEE:	Rules of the Road Committee (RORC)

TOPIC: 	Bicycle: overtaking on the right

STATUS / DATE OF ACTION:

BTC Draft:	07/10/2012

BTC Approval:	10/25/2012

Transmitted to Sponsors:	05/03/2013 (v0.1)

BTC Revision:

RORC Approval:

Council Approval:

ORIGIN OF REQUEST:	NCUTCD Bicycle Technical Committee

NCUTCD Rules of the Road Committee

AFFECTED SECTIONS OF UVC:	 11-304

# SUMMARY:

# This change modifies the rule for overtaking on the right, reflecting the rule in most states that bicyclists may ride on the shoulder.

# DISCUSSION:

As bicyclists may ride on the shoulder of the highway in most jurisdictions (and as clarified in proposed change to 11-1202), bicyclists should be permitted to overtake on the right on the shoulder under the same conditions that apply to any vehicle in the right-hand travel lane.

# RECOMMENDED CHANGES:

# Section 11-304 of the UVC is proposed to be modified as follows. Deletions from the 2000 UVC text are noted in strikethrough red, and insertions in underline blue.

§	11-304-When passing on the right is permitted

- The driver of a vehicle may overtake and pass upon the right of another vehicle only under one or more of the following conditions:

- When the vehicle overtaken is making or about to make a  left turn;

- Upon a roadway with unobstructed pavement of sufficient width for two or more lines of vehicles moving lawfully in the direction being traveled by the overtaking vehicle.

- The driver of a vehicle may overtake and pass another vehicle upon the right only under conditions permitting such movement in safety. Such movement shall not be made by driving off the roadway except that a person operating a bicycle may pass on the shoulder, provided the movement may be done in safety.