NOTE: In 2009, the National Committee on Uniform Traffic Laws and Ordinances (NCUTLO), which developed and maintained the Uniform Vehicle Code (UVC), went into hiatus. This left a void that the NCUTCD believes must be filled in order for its goal of uniformity of traffic control devices to be achieved and to provide guidance on model laws and rules for States and local governments. The Rules of the Road Committee (RORC) is an ad hoc committee of the NCUTCD to address changes to the “Rules of the Road” of the UVC.

Final recommended UVC content, as approved at a regular meeting of the NCUTCD, will be posted on the NCUTCD web site as model law for use by States and local jurisdictions wishing to have their Rules of the Road consistent with the national standard.  The recommendations, not being a part of the Manual on Uniform Traffic Control Devices, have no status with the FHWA.

TECHNICAL COMMITTEE:	Rules of the Road Committee (RORC)

TOPIC: 	Bicycle: headlight and taillight

STATUS / DATE OF ACTION:

BTC Draft:	07/10/2012

BTC Approval:

Transmitted to Sponsors:	(withdrawn from May2013 sponsor distribution)

BTC Revision:

RORC Approval:

Council Approval:

ORIGIN OF REQUEST:	NCUTCD Bicycle Technical Committee

NCUTCD Rules of the Road Committee

AFFECTED SECTIONS OF UVC:	 12-702

# SUMMARY:

# This change improves the language requiring headlights and taillights on bicycles..

# DISCUSSION:

A headlight and rear reflector are among the most important safety items required for bicycle operation at night. They must be given prominence in traffic law. A taillight is nearly as important. Some  clarifying provisions are needed. As to generator lights: they are common, and sufficient. When a bicycle is in motion, a headlight is essential to render the bicycle visible, because retroreflectors only send light back in the direction from which arrived. A vehicle entering from a side street, for example, does not have its headlights aimed at the bicycle. When the bicycle is in motion, retroreflectors are sufficient, because any vehicle which might collide with the bicycle is required to have a headlight which would then illuminate them

# RECOMMENDED CHANGES:

# Section 12-702 of the UVC is proposed to be modified as follows. Deletions from the 2000 UVC text are noted in strikethrough red, and insertions in underline blue.

§ 12-702 Headlight and taillight required at night

Every bicycle in use at the times described in 12-201 shall be equipped with a headlight on the front emitting a white light visible from a distance of at least 500 feet to the front and 300 feet to the sides, and a taillight on the rear emitting a steady or flashing red light visible from a distance of at least 1000 feet to the rear. A generator powered lamp, which emits light only when the bicycle is moving, may be used to meet the headlight requirements of this section. The headlight and taillight may be attached either to the bicycle or to the operator.