NOTE: The Rules of the Road Committee (RORC) was created by the Executive Committee as an adhoc committee of the NCUTCD to address changes the “Rules of the Road” of the Uniform Vehicle Code (UVC).  This occurred because the National Committee on Uniform Traffic Laws and Ordinances (NCUTLO) went into hiatus pending a viable funding source in June of 2009.  This left a void that the NCUTCD believes needs to be filled, and no other technical or professional group came forward to fund such an activity.  Even copies of the previous UVC are no longer available to provide guidance on such model laws and rules to States and local governments.  As individual changes are proposed and approved by sponsors and the NCUTCD, they will be posted on the NCUTCD web site as recommendations of the Committee.   The recommendations are not part of the MUTCD and as such have no status with the FHWA.

The RORC contains representatives of each of the Technical Committees.

COMMITTEE OF ORIGIN:	Rules of the Road Committee (RORC)

STATUS/DATE OF ACTION:	Send for Sponsor Comments

TOPIC: 	Right turns

RORC Approval:	_____, 2012

Transmitted to Sponsors:	_____, 2012

Council Approval:	_____, 2012

ORIGIN OF REQUEST:	John S. Allen, Bicycle Technical Committee member

AFFECTED SECTIONS OF UVC	 11-601

# SUMMARY:

# This change clarifies the requirement to merge to the right when there is a bike lane..

# The full unedited wording of the current section is shown below:

§	11-601 Required position and method of turning

The driver of a vehicle intending to turn shall do so as follows:

- Right turns - Both the approach for a right turn and a right turn shall be made as close as practicable to the right-hand curb or edge of the roadway.

- Left turns - The driver of a vehicle intending to turn left shall approach the turn in the extreme left lane lawfully available to traffic moving in the direction of travel of such vehicle. Whenever practicable, the left turn shall be made to the left of the center of the intersection so as to leave the intersection or other location in the extreme left lane lawfully available to traffic.

- (c) The state highway commission and local authorities in their respective jurisdictions may cause official traffic-control devices to be placed and thereby require and direct that a different course from  that specified in this section be traveled by turning vehicles, and when such devices are so placed no driver shall turn a vehicle other than as directed and required by such devices.

- (d) Two-way left-turn lanes - Where a special lane for making left turns by drivers proceeding in opposite directions has been indicated by official traffic-control devices:

- 1. A left turn shall not be made from any other lane.

- 2. A vehicle shall not be driven in the lane except when

- preparing for or making a left turn from or into the roadway or when preparing for or making a U turn when otherwise permitted by law.

# DISCUSSION:RECOMMENDED CHANGES TO “RULES OF THE ROAD, UVC”

Language added to §11-601(a) will help prevent the dangerous error called the “right hook”. This is similar to Calif. §21717

§	11-601 Required position and method of turning

The driver of a vehicle intending to turn shall do so as follows:

- Right turns - Both the approach for a right turn and a right turn shall be made as close as practicable to the right-hand curb or edge of the roadway. Where there is a separate lane for bicycles at the right edge of the roadway, a driver making a right turn must merge into this bicycle lane before turning, after yielding to any traffic that may be present.

- Left turns - The driver of a vehicle intending to turn left shall approach the turn in the extreme left lane lawfully available to traffic moving in the direction of travel of such vehicle. Whenever practicable, the left turn shall be made to the left of the center of the intersection so as to leave the intersection or other location in the extreme left lane lawfully available to traffic.

- (c) The state highway commission and local authorities in their respective jurisdictions may cause official traffic-control devices to be placed and thereby require and direct that a different course from  that specified in this section be traveled by turning vehicles, and when such devices are so placed no driver shall turn a vehicle other than as directed and required by such devices.

- (d) Two-way left-turn lanes - Where a special lane for making left turns by drivers proceeding in opposite directions has been indicated by official traffic-control devices:

- 1. A left turn shall not be made from any other lane.

- 2. A vehicle shall not be driven in the lane except when

- preparing for or making a left turn from or into the roadway or when preparing for or making a U turn when otherwise permitted by law.

VOTE: 	____ For, ____ Against, 	___ Abstentions