NOTE: The Rules of the Road Committee (RORC) was created by the Executive Committee as an adhoc committee of the NCUTCD to address changes to the “Rules of the Road” of the Uniform Vehicle Code (UVC).  This occurred because the National Committee on Uniform Traffic Laws and Ordinances (NCUTLO) went into hiatus pending a viable funding source in June of 2009.  This left a void that the NCUTCD believes needs to be filled, and no other technical or professional group came forward to fund such an activity.  Even copies of the previous UVC are no longer available to provide guidance on such model laws and rules to States and local governments.  As individual changes are proposed and approved by sponsors and the NCUTCD, they will be posted on the NCUTCD web site as recommendations of the Committee.   The recommendations are not part of the MUTCD and as such have no status with the FHWA.

The RORC is composed of representatives from each of the Technical Committees.

COMMITTEE OF ORIGIN:	Rules of the Road Committee(RORC)

STATUS/DATE OF ACTION:	Send for Sponsor Comments

TOPIC:

RORC Approval:	Jan. 2013

Transmitted to Sponsors:	Jan. 2013

Council Approval:	_____, 2013

ORIGIN OF REQUEST:

This request is the culmination of work by the Signals Technical Committee and the ROR Committee to

introduce and define the meaning of Flashing yellow and red arrows into the MUTCD.   That work was

completed with the publication of the 2009 MUTCD.   Since then, many states have begun using the

arrows, and there is no guidance in the previous UVC covering the actions of pedestrians and vehicles

facing such displays.  A complete overhaul of Chapter 11, Section 202, 203 and 204, UVC included below

has been completed and is being sent to sponsors for their comments.  Since similar language occurs for

Stop and Yield signs in Section 403, it too, needs to be updated to be compatible with the Signals portion

of the UVC and is also updated.  When completed, it will be published on the website of the NCUTCD,

along with other portions of Chapter 11 when approved as a recommendation of the NCUTCD for other

states and cities.  Some of the work of the Bicycle Technical Committee on Chapter 11 has also been

incorporated as well to be consistent with what that group has done.

AFFECTED SECTIONS OF UVC:  Chapter 11, Section 202, 203 and Section 403.

# SUMMARY:

# The previous language in the ROR, Chapter 11 is included in black, with additions proposed in underlined red.   A consistence of meaning is carried forward in each section, to make it clear to all road users what they are required to do.  This is also carried over to their actions at stop and yield signs.   Appropriate footnotes from the current ROR have been modified and retained where appropriate.

CHAPTER 11

Rules of the Road

§	11-202 Traffic Control Signal legends

In the event an official traffic control signal is erected and maintained at a place other than an intersection, the provisions of this section shall be applicable except as to those provisions which by their nature can have no application.  Any stop required shall be made at a sign or marking on the pavement indicating where the stop shall be made, but in the absence of any such sign or marking the stop shall be made at the signal.

Whenever traffic is controlled by traffic—control signals exhibiting different colored lights, or colored lighted arrows, successively one at a time or in combination, only the colors Green, Red and Yellow shall be used, except for special pedestrian signals carrying a legend and except for special bicycle signals carrying a legend, and said lights shall indicate and apply as follows:

- Green indication:

- Vehicular traffic facing a circular green signal indication may proceed straight through or turn right or left or make a U-turn movement except as such movements are modified or prohibited by other traffic control devices. unless a sign at such place prohibits either such turn

But vehicular traffic, including vehicles turning right or left, shall yield the right of way to other vehicles and to pedestrians lawfully within the intersection or an adjacent crosswalk at the time such signal is exhibited.

At the time such signal indication is exhibited, vehicular traffic, including vehicles turning right or left or making a U-turn movement, shall yield the right-of-way to:

  - Pedestrians lawfully within the intersection or an associated crosswalk, and

(b)	To bicyclists lawfully on the roadway or a crosswalk or path crossing, and

(c)	To other vehicles lawfully within the intersection, and

(d)	To other vehicles approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning vehicle is moving across or within the intersection.

2.	Vehicular traffic facing a green arrow signal indication73, shown alone or in combination with another traffic signal indication may cautiously enter the intersection only to make the movement indicated by such arrow, or such other movement as is permitted by other indications shown the same time.  Such vehicular traffic shall yield the right of way to pedestrians lawfully within an adjacent crosswalk and to other traffic lawfully using the intersection.

At the time such signal indication is exhibited, vehicular traffic, including vehicles turning right or left or making a U-turn movement, shall yield the right-of-way to:

- Pedestrians lawfully within the intersection or an associated crosswalk, and

(b)	To bicyclists lawfully on the roadway or in a crosswalk or path crossing, and

(c)	To other vehicles lawfully within the intersection, and

(d)	To other vehicles approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning vehicle is moving across or within the intersection.

3.	Unless otherwise directed by a pedestrian-control signal as provided in §11-203, pedestrians facing any circular green signal indication, may proceed across the roadway within any marked or unmarked crosswalk. Such pedestrians shall yield the right-of-way to vehicles lawfully within the intersection or so close as to constitute an immediate hazard at the time that the green signal indication is first exhibited.

4.	Unless otherwise directed by a pedestrian control signal as provided in §11-203, pedestrians facing only a green arrow signal indication shall not enter or cross the roadway.

5.	Unless otherwise directed by a bicycle-control signal as provided in §11-xxx, bicycle operators facing a circular green signal indication may proceed across the intersection on the roadway or on a marked bicycle crossing but bicycle riders facing a green arrow signal indication may proceed only in the direction indicated by said green arrow.

________________________________

73 It is recommended that the display of a turning green arrow indication alone or with another indication should indicate that during this display the turning movement is not interfered with by oncoming traffic, which simultaneously should face a red signal.

(b)	Steady yellow indication74

1.	Vehicular traffic facing a steady circular yellow or yellow arrow signal indication is thereby warned that the related green movement or the related flashing arrow movement is being modified or terminated or that a red indication will be exhibited immediately thereafter.  The rules set forth concerning vehicular, pedestrian, and bicycle operation under the movement(s) being modified or terminated shall continue to apply while the steady circular yellow signal indication is exhibited.

A steady red signal indication may be exhibited immediately thereafter when traffic shall not enter the intersection.  Or a flashing arrow may be exhibited immediately thereafter, whereby the movement being modified may continue under the rules applicable to the flashing arrow being then exhibited.

- Vehicular traffic facing a steady yellow arrow signal indication is thereby warned that the related green arrow movement or the related flashing arrow movement is being modified or terminated.  The rules set forth concerning operation under the movement(s) being modified or terminated shall continue to apply while the steady yellow arrow signal indication is exhibited.

A steady red signal indication may be exhibited immediately thereafter when shall not enter the intersection.  Or a flashing arrow may be exhibited immediately thereafter whereby the movement being modified may continue under the rules applicable to the flashing arrow being then exhibited.

3.	Unless otherwise directed by a pedestrian-control signal as provided in §11—203, pedestrians facing a steady circular yellow or yellow arrow signal indication, are thereby advised warned that there is insufficient time to cross the roadway before the next signal indication a red indication is shown is exhibited and no pedestrian shall then start to cross the roadway.

4.	Unless otherwise directed by a bicycle-control signal as provided in §11-xxx, bicycle riders facing a steady circular yellow or yellow arrow signal indication shall operate as directed in subsection (b)1 or (b)2.

_____________________

74 It is recommended that the color yellow not be used only before red If yellow is used following the red. Traffic facing the signal notified of a pending green or flashing arrow indication has a tendency to start before the green or flashing arrow signal appears indication is exhibited, causing interference with cross traffic clearing the intersection.

(c)	Steady red indication

1.	Vehicular traffic facing a steady circular red signal indication alone shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then before entering the intersection, and shall remain standing until an indication to proceed is shown except as provided in subsection (c)3.

2.	Vehicular traffic facing a steady red arrow signal indication shall not enter the intersection to make the movement indicated by the arrow, and unless entering the intersection to make a movement permitted by another signal, shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then before entering the intersection and shall remain standing until an indication permitting the movement indicated by such red arrow indication is shown exhibited except as provided in subsection (c)3.

3.	Except when a traffic control device is in place prohibiting a turn on red or a steady red arrow indication is displayed exhibited, vehicular traffic facing any steady circular red signal may cautiously enter the intersection to turn right, or to turn left from a one-way street into a one-way street, after stopping as required by subsection (c)1 or subsection (c)2.  After stopping the driver shall yield the right-of-way to any vehicle or in the intersection or approaching on another roadway so closely as to constitute an immediate hazard during the time such driver is moving across or within the intersection or junction of roadways. Such driver shall yield the right of way to pedestrians within the intersection or an adjacent crosswalk right to proceed with the turn shall be subject to the rules applicable after making a stop at a stop sign.

4.	Unless otherwise directed by a pedestrian control signal as provided in §11—203,  pedestrians facing a steady circular red or red arrow signal indication alone shall not enter or cross the roadway.

5.	Unless otherwise directed by a bicycle-control signal as provided in §11-xxx, bicycle operators facing a steady circular red or red arrow signal indication, shall not enter or cross the roadway.

6.  The operator of a vehicle who is facing a traffic control signal that is not displaying any indication may proceed  with caution, after yielding to all traffic lawfully in the intersection, subject to the rules after making  a stop at a stop sign (Section 11-403b).

7.  A vehicle facing a steady red signal which fails to change to green within a reasonable period of time and is non-responsive due to a signal malfunction or failure to detect its presence, shall stop before entering the intersection and may proceed with caution after yielding the right of way to all other traffic, subject to the rules after making  a stop at a stop sign (Section 11-403b).

(Committee note: Traffic signals may be inoperative or nonresponsive. A bicyclist, motorcyclist, Amish buggy or any light weight vehicle, may have no option but to proceed through an intersection on a red traffic signal indication, as many traffic signals are triggered by electronic actuators which do not respond to such vehicles.)

(d)	Flashing yellow arrow signal indications

1.	Vehicular traffic, facing a flashing yellow arrow signal indication, exhibited alone or in combination with another signal indication, is permitted to cautiously enter the intersection only to make the movement indicated by such arrow, or other such movement as is permitted by other signal indications exhibited at the same time.

At the time such signal indication is exhibited, vehicular traffic, including vehicles turning right or left or making a U-turn movement, shall yield the right-of-way to:

- Pedestrians lawfully within the intersection or an associated crosswalk, and

(b)	To bicyclists lawfully on the roadway or an associated bicycle path crosswalk or path crossing, and

(c)	To other vehicles lawfully within the intersection, and

(d)	To other vehicles approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning vehicle is moving across or within the intersection.

- Unless otherwise directed by a pedestrian control signal as provided in §11—203, pedestrians facing a flashing yellow arrow signal indication may proceed across the roadway within any marked or unmarked associated crosswalk.  Pedestrians shall yield the right-of-way to vehicles lawfully within the intersection at the time that the flashing yellow arrow signal indication is first exhibited.

- Unless otherwise directed by a bicycle-control signal as provided in §11-xxx, bicycle operators facing a flashing yellow arrow signal indication exhibited alone may proceed under the rules set forth for vehicles in subsection 1. of this Section.

(e)	Flashing red arrow signal indications

1.	Vehicular traffic facing a flashing red arrow signal indication, exhibited alone or in combination with another signal indication, if intending to turn in the direction indicated by the arrow, shall stop at a clearly marked stop line; but if there is no stop line, before entering the crosswalk on the near side of the intersection; or if there is no crosswalk, at the point nearest the intersecting roadway where the driver has a view of approaching traffic on the intersecting roadway before entering the intersection.  After stopping the driver shall proceed only in the direction indicated by the arrow indication and the right to proceed shall be subject to the rules applicable after making a stop at a stop sign.

2.	Unless otherwise directed by a pedestrian control signal as provided in §11—203, pedestrians facing a flashing red arrow signal indication, are permitted to proceed across the roadway within any marked or unmarked associated crosswalk.  Pedestrians shall yield the right-of-way to vehicles lawfully within the intersection at the time that the flashing red arrow signal indication is first exhibited.

- Unless otherwise directed by a bicycle control signal as provided in §11-xxx, bicycle operators facing a flashing red arrow signal indication, if intending to turn in the direction indicated by the arrow, may proceed across the roadway under the rules set forth for vehicles in subsection 1. of this Section.

§	11—203—Pedestrian-control signals75

Whenever special pedestrian-control signals exhibiting the “Walk” or “Don’t Walk” or symbols of a “walking person” or “upraised palm” are in place, such signals shall indicate as follows:

- Flashing or steady Walk or Walking Person — Any pedestrian facing the this signal indication may proceed across the roadway in the direction of the pedestrian-control signal and every driver of a vehicle shall yield the right of way to such pedestrian, except that pedestrians shall yield the right-of-way to vehicles lawfully within the intersection at the time that this pedestrian signal indication is first exhibited.

- Flashing or Steady Don’t Walk or Upraised Palm — No pedestrian shall start to cross the roadway in the direction of the this flashing or steady signal indication, but any pedestrian who has partially completed crossing on the walking person signal indication shall proceed to a paved or unpaved sidewalk or safety island while the don’t walk or upraised palm signal indication is exhibited showing.

- Countdown Indication — Any pedestrian facing this signal indication exhibited alone or in combination with a flashing Upraised Palm may start to cross the roadway, but must reach the far side paved or unpaved sidewalk or a safety island before the countdown indication reaches zero.

(d)  For the purposes of this Section, a WALK indication may replace the Walking Person indication and a DONT WALK indication may replace the Upraise Palm indication.

_________________________

75 In jurisdictions states where pedestrian-control signals using the “Wait” word legends are still in use, subsection (d) authorization for these should be continued in the law until they are all replaced.

§	11—XXX—Bicycle-control signals

Whenever bicycle-control signals exhibiting the symbols of a “xxxxxxxx” or “yyyyyyy” or “zzzzzzz” are in place, such signals shall require obedience by bicycle riders as follows:

- “xxxxxxx” — Any bicycle operator facing this signal indication may proceed straight through or turn right or left or make a U-turn movement except as such movements are modified or prohibited by other traffic control devices.

At the time such signal indication is exhibited, bicycle operators, including those turning right or left or making a U-turn movement, shall yield the right-of-way to:

- Pedestrians lawfully within the intersection or an associated crosswalk, and

(b)	To other vehicles or bicycle riders lawfully within the intersection, and

(c)	To other vehicles and bicycle operators approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning bicycle operator is moving across or within the intersection.

- “yyyyyyy” — Any bicycle operator facing this signal indication is thereby warned that the related “xxxxxxx” movement is being terminated.  A steady “zzzzzzz” signal indication may be exhibited immediately thereafter when bicycle traffic shall not enter or cross the roadway.

- “zzzzzzz” — Any bicycle operator facing this signal indication shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then before entering the intersection, and shall remain standing until an indication to proceed is exhibited.

§	11—204—Flashing traffic signals

- This section shall not apply at railroad grade crossings.  Conduct of drivers of vehicles and of all other road users approaching railroad grade crossings shall be governed by the rules as set forth in §11—701 of this code.

- This section shall not apply to the flashing arrow indications of official traffic-control signals as set forth in §11—202 of this code except when the illuminated circular signal indications thereat are also illuminated with rapid intermittent flashes.

- In the event an official flashing traffic signal is erected and maintained at a place other than an intersection, the provisions of this section shall be applicable except as to those provisions which by their nature can have no application.  Any stop required shall be made at a sign or marking on the pavement indicating where the stop shall be made, but in the absence of any such sign or marking the stop shall be made at the signal.

- Whenever an illuminated flashing red or yellow indication light is exhibited used in a traffic signal, or with a traffic sign it shall require obedience by vehicular traffic road users as follows:

1.	Flashing red (stop signal)—When a red lens signal indication is illuminated with rapid intermittent flashes, drivers of vehicles facing said indications shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then at the point nearest the intersecting roadway where the driver has a view of approaching traffic on the intersecting roadway before entering it the intersection, and the right to proceed shall be subject to the rules applicable after making a stop at a STOP sign.

2.	Flashing yellow (caution signal)—When a yellow lens signal indication is illuminated with rapid intermittent flashes, drivers of vehicles facing said indications may proceed through the intersection or past such signal only with caution cautiously enter the intersection to proceed straight through or turn right or left or make a U-turn except as such movement are modified or prohibited by other traffic control devices.

At the time such signal indication is exhibited, vehicular traffic, including those turning right or left or making a U-turn movement, shall yield the right-of-way to:

- Pedestrians lawfully within the intersection or an associated crosswalk, and

(b)	To bicycle riders lawfully on the roadway or a crosswalk or path crossing, and

(c)	To other vehicles lawfully within the intersection, and

(d)	To other vehicles approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning vehicle is moving across or within the intersection.

- When drivers of vehicles intend to proceed in the direction indicated by a flashing arrow indication, they shall proceed in the intended direction under the rules set forth in subsections 1. or 2. of this Section.

- Unless otherwise directed by a pedestrian control signal as provided in §11—203, pedestrians facing a flashing signal indication, may proceed across the roadway within any marked or unmarked associated crosswalk.

§	11—403—Stop signs and Yield signs

(a)	Preferential right of way may be indicated by stop signs or yield signs as authorized in §15—109 of this code.

(b)	Except when directed to proceed by a police officer, every driver of a vehicle approaching a stop sign shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then at the point nearest the intersecting roadway where the driver has a view of approaching traffic on the intersecting roadway before entering it. After having stopped, the driver shall yield the right of way to: any vehicle in the intersection or approaching on another roadway so closely as to constitute an immediate hazard during the time when such driver is moving across or within the intersection or junction of roadways. Such driver shall yield the right of way to pedestrians within an adjacent crosswalk.

(1)	Pedestrians lawfully within the intersection or an associated crosswalk, and

(2)	To bicyclists lawfully on the roadway or a crosswalk or path crossing, and

(3)	To other vehicles lawfully within the intersection, and

(4)	To other vehicles approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning vehicle is moving across or within the intersection.

(c)	The driver of vehicle approaching a yield sign shall in obedience to such sign slow down to a speed reasonable for the existing conditions, and if required for safety to stop, shall stop at a clearly marked stop line, but if none, before entering the crosswalk on the near side of the intersection, or if none, then at the point nearest the intersecting roadway where the driver has a view of approaching traffic on the intersecting roadway before entering it.  After slowing or stopping, the driver shall yield the right of way to: any vehicle in the intersection or approaching on another roadway so closely as to constitute an immediate hazard during the time such driver is moving across or within the intersection or junction of roadways. Such driver shall yield the right of way to pedestrians within an adjacent crosswalk.

(1)	Pedestrians lawfully within the intersection or an associated crosswalk, and

(2)	To bicyclists lawfully on the roadway or a crosswalk or path crossing, and

(3)	To other vehicles lawfully within the intersection, and

(4)	To other vehicles approaching from the opposite direction so closely as to constitute an immediate hazard during the time when such turning vehicle is moving across or within the intersection.

If such a driver after driving past a yield sign is involved in a collision with a vehicle  in the intersection or junction of roadways or with a pedestrian or lawful vehicle operator  in a crosswalk or path crossing, such collision shall be deemed prima facie evidence of the driver’s failure to yield right of way.

(d)	Except when directed to proceed by a police officer, every driver of a vehicle approaching a stop sign located at a railroad crossing shall stop at the clearly marked stop line, but if none, before entering the crosswalk on the near side of the crossing, or if none, then within 50 feet but not less than 15 feet from the nearest rail of such railroad and while so stopped shall listen and look in both directions along such track for signals indicating the approach of a train or other vehicle, and shall not proceed until it is safe to do so. After stopping as required herein and proceeding when it is safe to do so, the driver shall cross only in such gear of the vehicle that there will be no necessity for manually changing gears while traversing such crossing, and the driver shall not manually shift gears while crossing the track or tracks.

# DISCUSSION:RECOMMENDED CHANGES TO “RULES OF THE ROAD, UVC”

# It is important to get this out for comment and adoption, as three years have elapsed since the 2009 MUTCD.

VOTE: 	__7__ For, __0__ Against, 	__0_ Abstentions

# Comments

Deleted because

- “Person operating a bicycle” is distinct from “bicycle rider” (who may not be in control of the bicycle – e.g., the person on the rear of a tandem or a child in a child seat).

- Bicycles are defined as vehicles in the UVC, In states where the bicycle is defined as a device, bicyclists have the rights and duties of vehicle operators. The separate naming of “driver of vehicle” and “bicycle rider” is redundant.

- The rights and duties of the different classes of operators, and pedestrians, are spelled out in the text below.

Bicyclists may lawfully ride in crosswalks. Most paths are shared-use paths, not “bicycle paths”. A common use of bicycle signals occurs where a path crosses a street, but there is no associated street crossing.

Again, redundant, and the olvelapping definitions of “bicycle” and “vehicle” pose a problem.

Again, redundant

And again. The main problem here is that bicycles should not be described as if they were not vehicles. Rules for bicyclists are only different in the relatively few cases where there are separate bicycle signals.

This replaces one of the suggestions made by the Bicycle Technical Committee.

Redundant, and so, can lead to confusion. Bicycles are defined as vehicles. Perhaps a note should be added that in states where bicycles are defined as devices, and bicycle operators have the rights and duties of vehicle operators, the words “and operators of bicycles” should be added, even though it is redundant, as this section spells out thorights and duties of vehicle operators!

See previous comment.

I see one unresolved issue here: that other classes of vehicles besides bicycles are permitted on some paths: snowmobiles, human-powered vehicles as distrinct from bicycles; push scooters etc.

Here, bicycles are not called out separately. That would be unnecessary, as it is elsewhere.